## Slide 1
ISEG NATIONAL CONFERENCE EGCON-2018
3rd-5th December,2018
GSI, TI,SR, Hyderabad

## Slide 2
Soil Mechanics: Consistency Test Data for Subsurface Investigation & liquefaction. A Case Study of Pondicherry Seismic Microzonations.
S. P. Dhanvijay, Director, Project Landslide, GSI-NER, Dimapur
&
B. Ajaya Kumar, Director, EG Division, SR, Hyderabad.

## Slide 3
Seismic Microzonations attended by GT Lab SR,Hyderabd
Seismic microzonation of Vijayawada
Seismic microzonation of Vishakhapatnam
Seismic microzonation of Chennai
Seismic microzonation of Kochin
Seismic microzonation of Mangalore

## Slide 4
Introduction
Seismic hazard Microzonation of Pondicherry, India was carried out during 2005-07 in an area of about 150 sq.km in Survey of India Toposheet No.58M/13/1&2 to classify the urban agglomeration into different discrete zones of seismic hazard. The Pondicherry area is essentially a plain country with an upland area of Cuddalore sandstone with its immediate vicinity covered by soil/alluvial overburden underlain apparently by geotechnically not so competent Cuddalore sandstone. The plains essentially comprise of coastal and older flood plains of the Gingee River and the Ariyankuppam River. Of the 11 boreholes drilled in Pondicherry area, 4 are over Tidal flats, 3 are over beach dune, 4 are over flood plain, aggregating to a depth of 325m. In all about 1104 SPT are carried out up to a depth of 30m at an average interval of 2m, indicated a loose to moderately dense soil media up to an average depth of about 14 to 16m.

## Slide 5
Targets and analysis
Analysis of 104 SPT samples (carried out up to a depth of 30m at an average interval of 2m)
Analysis of 74 bulk samples carried out for Atterberg and consistency test data parameters
The grain size weight percent determination for different bore holes drilled in Pondicherry area.
The grain size distribution curves for soil samples received from different borehole locations of Pondicherry area.
Synthesization of geotechnical input to the assessment of the liquefaction potential / susceptibility of sub surface soil media.
Classification of soils for potentially vulnerable to seismically induced liquefaction.

## Slide 6
SPT & Bulk samples received and analysed by
GT Lab SR,Hyderabd
S.No | Nature of sample | Name of the project | Sample received | Total parameter analysed
1 | SPT | Seismic Microzonation of Pondicherry agglomeration, Pondicherry, Earthquake Geology Div,GSI SR,Hyderabd. | 58 | 406
2 | SPT |  | 44 | 300
3 | Bulk |  | 41 | 320
4 | Bulk |  | 33 | 231
 | Total |  | 176 | 1257

## Slide 7
Analysis table(CL-ML)
S.No | Sample No | LL | PL | PI | SL | Co | Friction angle Ø | Group symbol | Remarks
 |  | % | % |  | % | kg/cm2 |  |  | 
1 | BH-P1/BS1 | 56 | 25 | 31 | 13 | 0.36 | 17 | CH | --
2 | BH-P1/BS2 | 24 | 13 | 11 | 15 | 0.29 | 26 | CL | --
3 | BH-P1/BS3 | 20 | -- | -- | -- | 0.36 | 22 | -- | Non Cohesive
4 | BH-P1/BS4 | 20 | 9 | 11 | 13 | 0.36 | 22 | CL | --
5 | BH-P1/BS5 | 17 | 12 | 5 | 11 | 0.3 | 25 | CL-ML | --
6 | BH-P1/BS6 | 20 | 13 | 7 | 12 | 0.24 | 32 | CL-ML | --
7 | BH-P1/BS7 | 17 | 13 | 4 | 12 | 0.22 | 30 | CL-ML | --
8 | BH-P1/BS8 | 17 | 15 | 2 | 13 | 0.22 | 30 | CL-ML | --
9 | BH-P1/BS9 | 19 | 15 | 4 | 14 | 0.22 | 32 | CL-ML | --
10 | BH-P1/BS10 | 16 | 14 | 2 | 13 | 0.26 | 27 | CL-ML | --
11 | BH-P2/BS1 | 39 | 24 | 15 | 17 | 0.36 | 28 | CL | --
12 | BH-P2/BS2 | 33 | 18 | 15 | 15 | 0.1 | 33 | CL | --
13 | BH-P2/BS3 | 27 | -- | -- | -- | 0.19 | 31 | -- | Non Cohesive
14 | BH-P2/BS4 | 25 | 23 | 2 | 21 | 0.26 | 31 | ML | --
15 | BH-P2/BS5 | 36 | 23 | 13 | 20 | 0.45 | 25 | CL | --
16 | BH-P2/BS6 | 28 | -- | -- | -- | 0.21 | 28 | -- | Non Cohesive
17 | BH-P2/BS7 | 68 | 37 | 31 | 11 | 0.38 | 16 | MH | --
18 | BH-P3/BS1 | 26 | -- | -- | -- | 0.34 | 16 | -- | Non Cohesive
19 | BH-P3/BS2 | 64 | 32 | 32 | 12 | 0.19 | 7 | MH | --
20 | BH-P3/BS3 | 25 | 20 | 5 | 18 | 0.34 | 5 | CL-ML | --

## Slide 8
Analysis table(CL-ML)
S.No | Sample No | LL | PL | PI | SL | Co | Friction angle Ø | Group symbol | Remarks
21 | BH-P3/BS4 | 38 | 24 | 14 | 18 | 0.26 | 16 | CL | --
22 | BH-P3/BS5 | 52 | 30 | 22 | 11 | 0.19 | 12 | MH | --
23 | BH-P3/BS6 | 48 | 28 | 20 | 13 | 0.4 | 28 | ML | --
24 | BH-P4/BS1 | 30 | -- | -- | -- | 0.19 | 36 | -- | Non Cohesive
25 | BH-P4/BS2 | 24 | 20 | 4 | 20 | 0.24 | 33 | CL-ML | --
26 | BH-P4/BS3 | 26 | 19 | 7 | 17 | 0.29 | 24 | CL-ML | --
27 | BH-P4/BS4 | 21 | -- | -- | -- | 0.2 | 34 | -- | Non Cohesive
28 | BH-P4/BS5 | 56 | 34 | 22 | 18 | 0.5 | 18 | MH | --
29 | BH-P4/BS6 | 18 | 15 | 3 | 15 | 0.32 | 27 | CL-ML | --
30 | BH-P5/BS1 | 25 | 20 | 5 | 20 | 0.18 | 30 | CL-ML | --
31 | BH-P5/BS2 | 29 | 14 | 15 | 13 | 0.26 | 25 | CL | --
32 | BH-P5/BS3 | 26 | 19 | 7 | 16 | 0.29 | 20 | CL-ML | --
33 | BH-P5/BS4 | 24 | -- | -- | -- | 0.21 | 32 | -- | Non Cohesive
34 | BH-P5/BS5 |  |  |  |  | 0.28 | 28 | -- | and sandy
35 | BH-P5/BS6 | 44 | 25 | 19 | 20 | 0.29 | 8 | CL | --
36 | BH-P6/BS1 | 19 | -- | -- | -- | 0.18 | 34 | -- | Non Cohesive
37 | BH-P6/BS2 | 21 | -- | -- | -- | 0.19 | 31 | -- | Non Cohesive
38 | BH-P6/BS3 | 28 | -- | -- | -- | 0.27 | 29 | -- | Non Cohesive
39 | BH-P6/BS4 | 57 | 32 | 25 | 17 | 0.38 | 18 | MH | --
40 | BH-P6/BS5 | 63 | 29 | 34 | 15 | 0.32 | 5 | CH | --
41 | BH-P6/BS6 | 18 | 15 | 3 | 14 | 0.28 | 28 | CL-ML | --

## Slide 9
S.No | Sample No | LL | PL | PI | SL | Co kg/cm2 | Friction angle Ø | Group symbol | Remarks
 |  | % | % |  | % |  |  |  | 
1 | BH-P7/BS1 | 27 | 21 | 6 | 17 | 0.35 | 11 | CL-ML | --
2 | BH-P7/BS2 | 30 | 18 | 12 | 14 | 0.22 | 20 | CL | --
3 | BH-P7/BS3 | 35 | 20 | 15 | 14 | 0.38 | 21 | CL | --
4 | BH-P7/BS4 | 27 | -- | -- | -- | 0.2 | 34 | -- | Non Cohesive
5 | BH-P7/BS5 | 76 | 38 | 38 | 10 | 0.56 | 17 | MH | --
6 | BH-P7/BS6 | 30 | 20 | 10 | 15 | 0.28 | 27 | CL | --
7 | BH-P7/BS7 | 56 | 29 | 27 | 12 | 0.63 | 20 | CH | --
8 | BH-P8/BS1 | 35 | 25 | 10 | 21 | 0.36 | 26 | ML | --
9 | BH-P8/BS2 | 29 | 19 | 10 | 18 | 0.23 | 34 | CL | --
10 | BH-P8/BS3 | 25 | 19 | 6 | 18 | 0.24 | 26 | CL-ML | --
11 | BH-P8/BS4 | 21 | -- | -- | -- | 0.23 | 32 | -- | Non Cohesive
12 | BH-P8/BS5 |  |  |  |  | 0.24 | 34 | -- | Not sufficient and sandy
13 | BH-P8/BS6 | 20 | 13 | 7 | 14 | 0.24 | 25 | CL-ML | --
Analysis table(CL-ML)

## Slide 10
S.No | Sample No | LL | PL | PI | SL | Co kg/cm2 | Friction angle Ø | Group symbol | Remarks
14 | BH-P9/BS1 | 19 | -- | -- | -- | 0.28 | 29 | -- | Non Cohesive
15 | BH-P9/BS2 | 21 | -- | -- | -- | 0.24 | 26 | -- | Non Cohesive
16 | BH-P9/BS3 | 31 | -- | -- | -- | 0.26 | 26 | -- | Non Cohesive
17 | BH-P9/BS4 | 34 | 21 | 13 | 17 | 0.28 | 32 | CL | --
18 | BH-P9/BS5 | 47 | 23 | 24 | 19 | 0.35 | 11 | CL | --
19 | BH-P9/BS6 | 23 | -- | -- | -- | 0.31 | 24 | -- | Non Cohesive
20 | BH-P10/BS1 | 26 | 21 | 5 | 18 | 0.31 | 23 | CL-ML | --
21 | BH-P10/BS2 | 42 | 23 | 19 | 13 | 0.38 | 10 | CL | --
22 | BH-P10/BS3 | 40 | 23 | 17 | 14 | 0.34 | 22 | CL | --
23 | BH-P10/BS4 | 24 | -- | -- | -- | 0.26 | 24 | -- | Non Cohesive
24 | BH-P10/BS5 | 80 | 39 | 41 | 13 | 0.4 | 25 | MH | --
25 | BH-P10/BS6 | 26 | -- | -- | -- | 0.24 | 25 | -- | Non Cohesive
26 | BH-P10/BS7 | 41 | 21 | 20 | 16 | 0.3 | 15 | CL | --
27 | BH-P11/BS1 | 23 | -- | -- | -- | 0.27 | 29 | -- | Non Cohesive
28 | BH-P11/BS2 | 30 | -- | -- | -- | 0.24 | 28 | -- | Non Cohesive
29 | BH-P11/BS3 | 48 | 29 | 19 | 18 | 0.31 | 27 | ML | --
30 | BH-P11/BS4 | 33 | 18 | 15 | 18 | 0.24 | 29 | CL | --
31 | BH-P11/BS5 | 24 | 22 | 2 | 21 | 0.21 | 29 | ML | --
32 | BH-P11/BS6 | 31 | 16 | 15 | 13 | 0.24 | 30 | CL | --
33 | BH-P11/BS7 | 27 | -- | -- | -- | 0.25 | 31 | -- | Non Cohesive
Analysis table(CL-ML)

## Slide 11
MC and Grain size analysis
S.No | Sample no | Lab Ref. | MC % | Density | Specific gravity | Gravel | Sand | Silt | Clay
1 | P-1/SPT-1 | SM-1209 | 7.02 | 1.85 | 2.72 | .. | 82 | 18 | ..
2 | P-1/SPT-2 | SM-1210 | 10.83 | 1.97 | 2.61 | .. | 85 | 15 | ..
3 | P-1/SPT-3 | SM-1211 | 5.54 | 1.89 | 2.67 | 2 | 85 | 13 | ..
4 | P-1/SPT-4 | SM-1212 | 3.59 | 2.1 | 2.6 | 3 | 75 | 22 | ..
5 | P-1/SPT-5 | SM-1213 | 10.35 | 1.86 | 2.67 | 14 | 73 | 13 | ..
6 | P-1/SPT-6 | SM-1214 | 1.82 | 1.98 | 2.63 | 3 | 64 | 33 | ..
7 | P-1/SPT-7 | SM-1215 | 12.61 | 1.75 | 2.6 | 1 | 76 | 23 | ..
8 | P-1/SPT-8 | SM-1216 | 9.44 | 2.18 | 2.65 | 1 | 95 | 4 | ..
9 | P-2/SPT-1 | SM-1234 | 35.59 | 2.05 | 2.44 | .. | 51 | 49 | ..
10 | P-2/SPT-2 | SM-1235 | 21.98 | 1.87 | 2.62 | 1 | 66 | 33 | ..
11 | P-2/SPT-3 | SM-1236 | 13.15 | 2.66 | 2.69 | 1 | 90 | 9 | ..
12 | P-2/SPT-4 | SM-1237 | 23.11 | 2.28 | 2.52 | 7 | 73 | 20 | ..
13 | P-2/SPT-6 | SM-1238 | 44.25 | 1.9 | 2.42 | 7 | 63 | 30 | ..
14 | P-2/SPT-8 | SM-1239 | 42.21 | 1.72 | 2.58 | 1 | 78 | 21 | ..
15 | P-2/SPT-9 | SM-1240 | 45.06 | 1.36 | 2.47 | .. | 79 | 21 | ..
16 | P-2/SPT-10 | SM-1241 | 55.6 | 1.8 | 2.2 | 3 | 47 | 50 | ..
17 | P-2/SPT-11 | SM-1242 | 24.6 | 2.03 | 2.59 | .. | 66 | 34 | ..
18 | P-2/SPT-12 | SM-1243 | 40.88 | 1.81 | 2.22 | .. | 1 | 81 | 18
19 | P-3/SPT-1 | SM-1244 | 23.86 | 1.8 | 2.45 | 7 | 52 | 41 | ..
20 | P-3/SPT-2 | SM-1245 | 23.24 | 1.74 | 2.52 | 4 | 76 | 20 | ..

## Slide 12
MC and Grain size analysis
S.No | Sample no | Lab Ref. | MC % | Density | Specific gravity | Gravel | Sand | Silt | Clay
21 | P-3/SPT-3 | SM-1246 | 27.88 | 1.46 | 2.49 | .. | 48 | 52 | ..
22 | P-3/SPT-5 | SM-1247 | 20 | 2 | 2.56 | .. | 93 | 7 | ..
23 | P-3/SPT-6 | SM-1248 | 26.36 | 1.83 | 2.48 | 1 | 62 | 37 | ..
24 | P-3/SPT-7 | SM-1249 | 42.8 | 1.72 | 2.38 | 1 | 65 | 34 | ..
25 | P-3/SPT-8 | SM-1250 | 24.34 | 1.64 | 2.52 | 3 | 77 | 20 | ..
26 | P-3/SPT-9 | SM-1251 | 25.6 | 2.1 | 2.51 | 3 | 71 | 26 | ..
27 | P-3/SPT-10 | SM-1252 | 15.46 | 1.82 | 2.29 | .. | 7 | 83 | 10
28 | P-3/SPT-11 | SM-1253 | 28.14 | 1.9 | 2.44 | .. | 69 | 31 | ..
29 | P-3/SPT-12 | SM-1254 | 25.87 | 1.86 | 2.4 | 1 | 56 | 43 | ..
30 | P-4/SPT-1 | SM-1261 | 4.58 | 1.76 | 2.63 | 1 | 86 | 13 | ..
31 | P-4/SPT-2 | SM-1262 | 9.14 | 1.9 | 2.52 | 1 | 89 | 10 | ..
32 | P-4/SPT-3 | SM-1263 | 14.08 | 2.44 | 2.69 | 5 | 87 | 8 | ..
33 | P-4/SPT-5 | SM-1264 | 27.9 | 1.95 | 2.49 | 2 | 50 | 48 | ..
34 | P-4/SPT-7 | SM-1265 | 73.85 | 1.62 | 2.1 | .. | 2 | 80 | 18
35 | P-4/SPT-8 | SM-1266 | 47.41 | 1.87 | 2.27 | 10 | 20 | 70 | ..
36 | P-4/SPT-9 | SM-1267 | 23.14 | 2.09 | 2.61 | 2 | 81 | 17 | ..
37 | P-4/SPT-10 | SM-1268 | 19.73 | 2.07 | 2.6 | 1 | 89 | 10 | ..
38 | P-4/SPT-12 | SM-1269 | 21.74 | 1.92 | 3.48 | .. | 95 | 5 | ..
39 | P-4/SPT-13 | SM-1270 | 20 | 1.76 | 2.69 | .. | 94 | 6 | ..
40 | P-5/SPT-1 | SM-1274 | 15.26 | 2.17 | 2.49 | .. | 60 | 40 | ..

## Slide 13
MC and Grain size analysis
S.No | Sample no | Lab Ref. | Moisture content % | Density gm/cm3 | Specific gravity | Gravel | Sand | Silt | Clay
41 | P-5/SPT-2 | SM-1275 | 18.79 | 2.16 | 2.38 | 1 | 66 | 33 | ..
42 | P-5/SPT-3 | SM-1276 | 14.06 | 2.22 | 2.65 | 4 | 70 | 26 | ..
43 | P-5/SPT-4 | SM-1277 | 15.45 | 2.25 | 2.49 | 4 | 62 | 34 | ..
44 | P-5/SPT-5 | SM-1278 | 21.98 | 1.3 | 2.52 | 10 | 64 | 26 | ..
45 | P-5/SPT-6 | SM-1279 | 8.1 | 2.15 | 2.7 | 14 | 66 | 20 | ..
46 | P-5/SPT-9 | SM-1280 | 8.91 | 1.86 | 2.58 | 3 | 93 | 4 | ..
47 | P-5/SPT-10 | SM-1281 | 32 | 2.08 | 2.4 | 20 | 65 | 15 | ..
48 | P-5/SPT-11 | SM-1282 | 11.95 | 2.45 | 2.66 | 33 | 53 | 14 | ..
49 | P-5/SPT-13 | SM-1283 | 10.04 | 2.42 | 2.5 | 4 | 91 | 5 | ..
50 | P-6/SPT-1 | SM-1284 | 6.9 | 1.73 | 2.84 | .. | 87 | 13 | ..
51 | P-6/SPT-2 | SM-1285 | 7.32 | 1.88 | 2.67 | 1 | 95 | 4 | ..
52 | P-6/SPT-3 | SM-1286 | 8.47 | 2.12 | 2.64 | .. | 88 | 12 | ..
53 | P-6/SPT-5 | SM-1287 | 23.71 | 1.95 | 2.91 | 13 | 63 | 24 | ..
54 | P-6/SPT-6 | SM-1288 | 18.44 | 1.95 | 2.54 | 10 | 21 | 69 | ..
55 | P-6/SPT-7 | SM-1289 | 32.9 | 1.84 | 2.44 | 1 | 8 | 69 | 22
56 | P-6/SPT-8 | SM-1290 | 31.15 | 1.88 | 2.29 | 7 | 25 | 68 | ..
57 | P-6/SPT-12 | SM-1291 | 14.86 | 1.7 | 2.45 | 1 | 81 | 18 | ..
58 | P-6/SPT-13 | SM-1292 | 17.2 | 2.03 | 2.74 | 1 | 86 | 13 | ..

## Slide 14
MC and Grain size analysis
S.No | Sample | Lab Ref. | MC % | Density gm/cm3 | Specific gravity | Gravel | Sand | Silt | Clay
1 | P-7/SPT-1 | SM-1309 | 17.94 | 1.48 | 2.63 | .. | 66 | 34 | ..
2 | P-7/SPT-2 | SM-1310 | 9.96 | 2.03 | 2.45 | 1 | 88 | 11 | ..
3 | P-7/SPT-3 | SM-1311 | 32.46 | 1.93 | 2.42 | .. | 43 | 57 | ..
4 | P-7/SPT-4 | SM-1312 | 30.27 | 1.92 | 2.4 | .. | 69 | 31 | ..
5 | P-7/SPT-5 | SM-1313 | 36.72 | 1.97 | 2.39 | 3 | 48 | 49 | ..
6 | P-7/SPT-6 | SM-1314 | 43.1 | 1.9 | 2.4 | .. | 32 | 68 | ..
7 | P-7/SPT-7 | SM-1315 | 33.04 | 1.69 | 2.41 | .. | 20 | 80 | ..
8 | P-7/SPT-8 | SM-1316 | 72.33 | 1.78 | 2.33 | .. | 25 | 75 | ..
9 | P-7/SPT-9 | SM-1317 | 53.71 | 1.9 | 2.56 | .. | 14 | 76 | 10
10 | P-7/SPT-10 | SM-1318 | 29.08 | 1.66 | 2.56 | .. | 4 | 80 | 16
11 | P-7/SPT-11 | SM-1319 | 23.57 | 1.74 | 2.48 | .. | 3 | 83 | 14
12 | P-7/SPT-14 | SM-1320 | 24.9 | 1.91 | 2.55 | .. | 72 | 28 | ..
13 | P-8/SPT-1 | SM-1321 | 11.4 | 2.01 | 2.41 | 1 | 39 | 60 | ..
14 | P-8/SPT-2 | SM-1322 | 16.45 | 1.86 | 2.47 | .. | 64 | 36 | ..
15 | P-8/SPT-3 | SM-1323 | 19.59 | 1.4 | 2.6 | .. | 64 | 36 | ..
16 | P-8/SPT-4 | SM-1324 | 16.08 | 2.12 | 2.55 | .. | 61 | 39 | ..
17 | P-8/SPT-5 | SM-1325 | 15.08 | 2.03 | 2.62 | 10 | 66 | 24 | ..
18 | P-8/SPT-6 | SM-1326 | 17.39 | 2.23 | 2.72 | 1 | 67 | 32 | 
19 | P-8/SPT-9 | SM-1327 | 12.18 | 2.06 | 2.67 | 5 | 91 | 4 | ..
20 | P-8/SPT-10 | SM-1328 | 21.01 | 2.1 | 2.61 | 1 | 97 | 2 | ..

## Slide 15
MC and Grain size analysis
S.No | Sample | Lab Ref. | Moisture content % | Density gm/cm3 | Specific gravity | Gravel | Sand | Silt | Clay
21 | P-8/SPT-11 | SM-1329 | 12.14 | 2.15 | 2.68 | 1 | 86 | 13 | ..
22 | P-9/SPT-1 | SM-1330 | 4.3 | 1.78 | 2.56 | .. | 87 | 13 | ..
23 | P-9/SPT-3 | SM-1331 | 21.16 | 2.34 | 2.7 | 5 | 82 | 13 | ..
24 | P-9/SPT-4 | SM-1332 | 24.59 | 1.98 | 2.48 | 10 | 56 | 34 | ..
25 | P-9/SPT-7 | SM-1333 | 58.08 | 1.8 | 2.22 | .. | 11 | 80 | 9
26 | P-9/SPT-9 | SM-1334 | 38.21 | 2.13 | 2.72 | 1 | 48 | 51 | ..
27 | P-9/SPT-10 | SM-1335 | 14.71 | 2.42 | 2.62 | 1 | 74 | 25 | 
28 | P-9/SPT-12 | SM-1336 | 33.74 | 2.62 | 2.68 | .. | 44 | 56 | ..
29 | P-10/SPT-1 | SM-1337 | 27.44 | 1.88 | 2.63 | .. | 13 | 82 | 5
30 | P-10/SPT-2 | SM-1338 | 18.88 | 2 | 2.5 | .. | 61 | 39 | ..
31 | P-10/SPT-3 | SM-1339 | 19.05 | 2.2 | 2.56 | .. | 62 | 38 | ..
32 | P-10/SPT-5 | SM-1340 | 16.66 | 2.38 | 2.62 | 16 | 56 | 28 | ..
33 | P-10/SPT-6 | SM-1341 | 16.25 | 2.24 | 2.58 | 1 | 72 | 27 | ..
34 | P-10/SPT-8 | SM-1342 | 18 | 1.8 | 2.43 | 7 | 65 | 28 | 
35 | P-10/SPT-9 | SM-1343 | 49.17 | 1.69 | 2.29 | 25 | 5 | 70 | ..
36 | P-10/SPT-10 | SM-1344 | 61.08 | 2.05 | 2.23 | 2 | 4 | 86 | 8
37 | P-10/SPT-11 | SM-1345 | 23.68 | 1.94 | 2.58 | .. | 84 | 16 | ..
38 | P-10/SPT-12 | SM-1346 | 21.25 | 2.24 | 2.54 | .. | 90 | 10 | ..
39 | P-11/SPT-3 | SM-1347 | 13.33 | 2.25 | 2.64 | .. | 85 | 15 | ..
40 | P-11/SPT-4 | SM-1348 | 13.56 | 2.15 | 2.65 | 3 | 86 | 11 | ..
41 | P-11/SPT-5 | SM-1349 | 40.16 | 2.18 | 2.64 | 2 | 80 | 18 | ..
42 | P-11/SPT-6 | SM-1350 | 16.48 | 2.55 | 2.5 | 2 | 68 | 30 | ..
43 | P-11/SPT-7 | SM-1351 | 19.68 | 1.9 | 2.76 | 23 | 27 | 50 | ..
44 | P-11/SPT-8 | SM-1352 | 15.2 | 1.3 | 2.61 | 6 | 54 | 40 | ..

## Slide 16
Plasticity chart with zones recommended by Seed et al. with Atterberg results plotted.

## Slide 17
Observation & Conclusion

## Slide 18
Interpretation
In all about 95 SPT carried out up to a depth of 30m at an average interval of 2m, indicated a loose to moderately dense soil media up to an average depth of about 14 to 16 with N value between 5 and 30.
By synthesizing the geotechnical inputs, Microzones of area of the undisturbed samples, were analyzed to determine the soil mechanical properties, as an input to the assessment of the liquefaction potential / susceptibility of sub surface soil media.
The grain size weight percent determined at various depths in different bore hole locations of Pondicherry area indicated that the silty sand, sandy silt, and silt and silty clay are the dominant soil fractions in the area under investigation.
The grain size distribution curves of soil samples observed in different borehole locations of Pondicherry area showed that the tendency of the respective curves towards close to the boundary of potentially liquefiable soils.
The relatively clean sandy soils with few fines are potentially vulnerable to seismically induced liquefaction.

## Slide 19
Conclusions
The soil present in borehole no-01,03,05,06,08, is containing less than 15-20% particles by weight, smaller than 0.005 mm, and having a water content (WC) to liquid limit (LL) ratio greater than 0.9 is susceptible to liquefaction.
Clayey soils is susceptible to liquefaction as of the following conditions are met: (1) percent of particles less than 0.005 mm <15%,
(2) LL<35%, and
(3) WC/LL>0.9
Hence treated as a simple criteria based on soil parameters determinations to deduce the susceptibility of liquefaction in fine grained soils present in above mentioned boreholes.
The grain size of silts falls between that of sand and clay, it is often assumed that the susceptibility of silts must also fall somewhere between the high susceptibility of sands which may prone to liquefaction.

## Slide 20
Observation & Conclusion
In this paper, the geotechnically analysed soils are considered to be of potentially liquefiable type with character of: (1) less than 15% “clay” fines 0.005 mm), (2) Liquid Limit of LL ≤35%, and (3) water content greater than or equal to 90% of the Liquid Limit (seed e tal 1984-85).
Andrews and Martin (2000) also recommend that soils with less than about 10% clay fines (< 0.002 mm) and a Liquid Limit(LL) in the minus #40 sieve fraction of less than 32% be considered potentially liquefiable, that soils with more than about 10% clay fines and LL≥32% are unlikely to be susceptible to classic cyclically-induced liquefaction. Even this principle is also applicable to the studies carried out for Pondicherry seismic microzonations.

## Slide 21
THANK YOU